## Slide 1: Lecture 1.3 AI Hardware
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
Compute Internals
CPU Internals
Arm and Intel CPUs
GPU Computing

## Slide 4: Learning Objectives
Describe the different types of hardware implementations for AI computing such as Edge, Embedded, Cloud and On-Premise.
Describe the difference between CPU and GPU processing
Write and execute code and compare differences between CPU and GPUs

## Slide 5: AI Hardware

## Slide 6: Computing Implementations
Cloud – Data is external to your network and accessed over HTTP
Edge – Access Data at the Edge of your Network or from the Device
On-Premise Data is located within your local network
AIoT – Artificial Intelligence of Things – AI and Internet of Things combined
Embedded-Data is local on the machine

## Slide 7: Compute Internals

## Slide 8: Computer Internal
These Photos by Unknown Author is licensed under CC BY-SA

## Slide 9: Operating System
Layer between Hardware and Software
Justice, Matthew. How Computers Really Work (p. 196). No Starch Press. Kindle Edition.

## Slide 10: Operating System Kernel
An operating system kernel is responsible for managing memory, facilitating device I/O, and providing a set of system services for applications. The kernel allows multiple programs to run in parallel and share hardware resources. It is the core part of an operating system, but it alone provides no way for end users to interact with the system.
Operating systems also include non-kernel components that are needed for a system to be of use. This includes the shell, a user interface for working with the kernel. The terms shell and kernel are part of a metaphor for operating systems, where the OS is thought of as a nut or seed. The kernel is at the core; a shell surrounds it.
Justice, Matthew. How Computers Really Work (pp. 195-196). No Starch Press. Kindle Edition.

## Slide 11: Hardware Interface
The shell can be either a command line interface (CLI) or a graphical user interface (GUI). Some examples of shells are the Windows shell GUI (including the desktop, Start menu, taskbar, and File Explorer), and the Bash shell CLI found on Linux and Unix systems.
When it comes to interacting with hardware, the kernel acts in partnership with device drivers. A device driver, or simply driver, is software designed to interact with specific hardware. An operating system’s kernel needs to work with a wide variety of hardware, so rather than designing the kernel to know how to interact with every hardware device in the world, software developers implement the code for specific devices in device drivers. Operating systems typically include a set of device drivers for common hardware and also provide a mechanism for installing additional drivers.
Justice, Matthew. How Computers Really Work (p. 196). No Starch Press. Kindle Edition.

## Slide 12: Components in an Operating System
Justice, Matthew. How Computers Really Work No Starch Press. Kindle Edition.

## Slide 13: Input/Output Operations
Computers need to interact with external environment
I/O Devices
OS has software device drivers for each device

## Slide 14: Nano Carrier Board Layout
ref: https://docs.NVIDIA.com/jetson/l4t/index.html#page/Tegra%20Linux%20Driver%20Package%20Development%20Guide/hw_setup.html#wwpID0E0YR0HA
Top View
Bottom View

## Slide 15: Jetson Board Support Architecture

## Slide 16: Jetson Board Support Architecture
Jetson Board Support Package
•Linux Kernel: A UNIX-like computer operating system kernel mostly used for mobile devices.
•Sample Root Filesystem derived from Ubuntu: A sample root filesystem of the Ubuntu distribution. Helps you create root filesystems for different configurations.
•Toolchain: A set of development tools chained together by stages that runs on various architectures.
•Bootloader: Boot software boot for initializing the system on the chip.
•Sources: Source code for kernel and multimedia applications.
•NVIDIA® Jetson™ User Space Drivers: Provides the NVIDIA drivers that run in the user space.
•Flashing Support Scripts and Tools: A set of scripts and associated tools to assist in flashing your system.
•Sample Source Code and Applications: Sample source code for developing embedded applications for the Jetson platform.
For additional descriptions, see: https://docs.NVIDIA.com/jetson/l4t/index.html#page/Tegra%20Linux%20Driver%20Package%20Development%20Guide/overview.html#
Package Descriptions

## Slide 17: Processors

## Slide 18: Processors
CPU – Central Processing Units
GPU – Graphics Processing Units
FPGA – Field Programmable Gate Arrays
ASIC – Application Specific Integrated Circuits
Retrieved from AI hardware - What they are and why they matter in 2021 (roboticsbiz.com)

## Slide 19: Parallel Computing – Flynn’s Taxonomy*
SISD- Single Instruction Single Data computing system is a uniprocessor machine that executes single instruction on a single data stream (uniprocessor – earlier CPUs)
SIMD- Single Instruction Multiple Data is a computing system with several identical processors each with local memory and work under the control of a single instruction stream ( Modern CPUs & GPUs).
MISD- multiple instruction, single data – different operators on same data (none available commercially)
MIMD- Multiple instruction, multiple data (Sun/IBM SMP – Symmetric Multi-Processing Machines)
More info:
https://www.geeksforgeeks.org/difference-between-simd-and-mimd/
Computer Architecture | Flynn's taxonomy - GeeksforGeeks

## Slide 20: Processors
SIMD -Single Instruction Multiple Data. | MIMD -Multiple Instruction Multiple Data.
Less memory. | Large memory.
Less cost | Higher cost
Single decoder. | Multiple decoders.
Latent or tacit synchronization. | Accurate or explicit synchronization.
Synchronous programming. | Asynchronous programming.
Simple in complexity | More complex
Less efficient for performance | More efficient for performance

## Slide 21: Components of a CPU
CPU
Registers
ALU
Control Unit
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 22: Multicore CPU

## Slide 23: CPU Cores
PHYSICAL AND LOGICAL CORES Not all cores are equally capable of parallelism. A physical core is a hardware implementation of a core within a CPU. Logical cores represent the ability of a single physical core to run multiple threads at once (one thread per logical core). Intel refers to this capability as hyper-threading.
A computer with two physical cores, each with two logical cores, has a total of four logical cores and run four threads at once. Logical cores cannot achieve the full parallelism of physical cores.
Justice, Matthew. How Computers Really Work (p. 203). No Starch Press. Kindle Edition.

## Slide 24: Cloud vCore consideration
You decide to reserve a virtual instance with 4 vCores:
  How many physical processors are available?
  How many logical cores are available?
Notes: There are 4 logical cores. Cloud computing typically allocates the individual cores to virtual instances so 4 vCores may be equivalent to physical processor.

## Slide 25
Ref:
https://www.microcontrollertips.com/risc-vs-cisc-architectures-one-better/#:~:text=One%20of%20the%20major%20differences%20between%20RISC%20and,and%20CISC%20emphasizes%20efficiency%20in%20instructions%20per%20program.
https://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 26: ARM Processor
Retrieved from www.arm.com

## Slide 27: ARM vs Intel CPUs

## Slide 28: Jetson Nano Block Diagram
L1/L2 Cache
L1/L2 Cache
ISP
ISP
Video Ingest (VI)
PCIe x4
USB 3.0
CSI x4
CSI x4
CSI x4/x2
CSI x2
DSI
eDP
HDMI
Memory Controller Fabric
NV Encoder
NV Decoder
Compositor (VIC)
NV JPEG
Multimedia Complex
DRAM
Quad-core ARM Cortex-A57 MPCore processor

## Slide 29: GPUs

## Slide 30: GPU vs CPU
Mythbusters Demo GPU versus CPU - YouTube

## Slide 31: CPU
Latency – beginning to end duration of performing a single computation (*Tuomanen, 2018)
CPUs are engineered to reduce the latency of a single computation.
Computations are sequential
Fewer cores that are restricted with the number of processes it can compute and it handles those processes very fast
*Hands-On GPU Programming with Python and CUDA

## Slide 32: Accelerated Computing 10x Performance & 5x Energy Efficiency for HPC
CPU
Optimized for
Serial Tasks
GPU Accelerator
Optimized for
Parallel Tasks
CPU Strengths
Very large main memory
Very fast clock speeds
Latency optimized via large caches
Small number of threads can run very quickly
CPU Weaknesses
Relatively low memory bandwidth
Cache misses very costly
Low performance/watt
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit
Notes: NVIDIA

## Slide 33: GPU
Each core is much simpler than that of the CPU and each core on its own is not as fast as a CPU
It’s the number of cores that make a difference. GPU has hundreds to thousands of cores compared to a CPU which has 1 to 6 cores
Computations are done in parallel, asynchronously.
Still relies on CPU for managing and passing data
Programs must be rewritten to enable parallel processing

## Slide 34: Accelerated Computing 10x Performance & 5x Energy Efficiency for HPC
CPU
Optimized for
Serial Tasks
GPU Accelerator
Optimized for
Parallel Tasks
GPU Strengths
High bandwidth main memory
Significantly more compute resources
Latency tolerant via parallelism
High throughput
High performance/watt
GPU Weaknesses
Relatively low memory capacity
Low per-thread performance
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit
Click to add text

## Slide 35: Accelerator Nodes
PCIe
RAM
RAM
CPU and GPU have distinct memories
CPU generally larger and slower
GPU generally smaller and faster
CPU and GPU communicate via PCIe
Data must be copied between these memories over PCIe
PCIe Bandwidth is much lower than either memories
Emerging Tech - Nvlink
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit

## Slide 36
CPU
Optimized for
Serial Tasks
GPU Accelerator
Optimized for
Parallel Tasks
Accelerated Computing 10x Performance & 5x Energy Efficiency for HPC
© NVIDIA 2013
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit
Notes: NVIDIA Slide

## Slide 37: Winning Applications Use Both CPU and GPU
CPUs for sequential parts where latency matters
  CPUs can be 10X+ faster than GPUs for sequential code
GPUs for parallel parts where throughput wins
  GPUs can be 10X+ faster than CPUs for parallel code
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit

## Slide 38: What is Heterogeneous Programming?
Application Code
+
GPU
CPU
A few % of Code
A large % of Time
Compute-Intensive Functions
Rest of Sequential
CPU Code
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit

## Slide 39: Amdahl’s Law (*Tuomanen, 2018)
Speedup =
p= proportion of code that can be parallelizable
N= number of GPU cuda cores
1
(1 – p) + p / N
*Hands-On GPU Programming with Python and CUDA

## Slide 40: Speed v. Throughput
Speed
Throughput
*Images from Wikimedia Commons via Creative Commons
Which is better depends on your needs…
© NVIDIA 2013
Slide adapted from NVIDIA Accelerated Computing Teaching Kit

## Slide 41: Recommended NVIDIA DLI Lab
To learn more about GPUs and how they fit into the overall data center infrastructure, see the following DLI Lab.
Introduction to AI in the Datacenter https://courses.NVIDIA.com/courses/course-v1:DLI+L-DC-01+V1/about

## Slide 42
Thank You
Edge AI and Robotics Teaching Kit