## Slide 1: Lecture 1.4 Jetson Nano
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
Part 1
Unboxing
Flash SD with Jetson Image
Hardware setup and SD card install
First boot and setup – Headless Configuration
Part 2
Linux Review & WiFi Setup
Jetson Docker Container Setup
Connect to Jupyter Lab to access course materials for NVIDIA Lab

## Slide 4: Learning Objectives
Understand the different types of Jetson Developer Kits
Configure and Setup up Jetson Nano
Learn to check for free disk space
Understand and run commands to list, download, run and remove containers
Demonstrate two different ways to deploy code to Jetson Nano by uploading and unzipping zipped code files or retrieving from github
Execute code and modify where needed

## Slide 5: Learning Objectives
Be able to configure and set up Jetson Nano 2gb
Connect to Jetson Nano 2gb using serial micro-usb and wifi connectivity
Download and run NVIDIA Docker Container
Access Jupyter Lab hosted on Jetson Nano through your laptop using wifi

## Slide 6: Part 1
Flash, setup and configuration
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 7: NVIDIA Jetson Nano
This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 8: NVIDIA Jetson Nano 2GB
Leverage cutting edge GPU computing techniques
Cost effective
Build solutions that can be implemented to real use cases
Get exposure to Robotics

## Slide 9: THE JETSON FAMILY
for AI at the Edge and Autonomous System designs
Multiple modules - Same software
Full specs at developer.nvidia.com/jetson
7.5 – 15W
45mm x 70mm
JETSON TX2 NX
1.3 TFLOPS (FP16)
5 - 10W
45mm x 70mm
JETSON NANO
0.5 TFLOPS (FP16)
10 – 30W
100mm x 87mm
JETSON AGX XAVIER series
11 TFLOPS (FP16)
32 TOPS (INT8)
10 - 15W
45mm x 70mm
JETSON XAVIER NX
6 TFLOPS (FP16)
21 TOPS (INT8)
AI at the edge
Fully autonomous machines

## Slide 10: JETSON DEVELOPER KITS
for Engineers, Makers, and Learners
5W | 10W
0.5 TFLOPS (FP16)
$59
JETSON NANO 2GB
5W | 10W
0.5 TFLOPS (FP16)
$99
JETSON NANO
10W | 15W
6 TFLOPS (FP16) | 21 TOPS (INT8)
$399
JETSON XAVIER NX
10 | 15W | 30W
11 TFLOPS (FP16) | 32 TOPS (INT8)
$699
JETSON AGX XAVIER
Multiple developer kits - Same software
Full specs at developer.nvidia.com/jetson

## Slide 11
Developer Kit Technical Specifications | 
GPU | 128-core NVIDIA Maxwell™
CPU | Quad-core ARM® A57 @ 1.43 GHz
Memory | 2 GB 64-bit LPDDR4 25.6 GB/s
Storage | microSD (Card not included)
Video Encoder | 4Kp30 ¦ 4x 1080p30 ¦ 9x 720p30 (H.264/H.265)
Video Decoder | 4Kp60 ¦ 2x 4Kp30 ¦ 8x 1080p30 ¦ 18x 720p30 (H.264/H.265)
Connectivity | Gigabit Ethernet, 802.11ac wireless*
Camera | 1x MIPI CSI-2 connector
Display | HDMI
USB | 1x USB 3.0 Type A, 2x USB 2.0 Type A, 1x USB 2.0 Micro-B
Others | 40-pin header (GPIO, I2C, I2S, SPI, UART) 12-pin header (Power and related signals, UART) 4-pin fan header*
Mechanical | 100 mm x 80 mm x 29 mm

## Slide 12: Jetson Nano 2GB – Unboxing the Kit
We will work through connecting and configuring your Jetson Nano in class. Much of the materials is based on the Nano plus the Sparkfun DLI accessories which include a camera and 32 gb SD card. This kit can be obtained at https://www.sparkfun.com/products/17245.
Watch this video to get familiar with your development kit.
https://www.youtube.com/watch?v=dVGEtWYkP2c

## Slide 13: Jetson Nano Accessories
You need the following accessories for your Nano:
  MicroSD card- minimum 32GB
  Camera – USB or Rasberry Pi
  MicroUSB for connecting to host PC
  USB-c Power Supply 5.1V 3A Output (if you have one with a barrel jack, you will need to buy an adaptor or get a USB-c cable and connect it to a USB socket)

## Slide 14: Part 1 - Flash and Configure
The MicroSD Card will hold the essential operation system and instructions needed to control your Jetson. Our first step is to flash the drive with the software image from NVIDIA.
NVIDIA has provided step by step instructions at: https://developer.nvidia.com/embedded/learn/get-started-jetson-nano-2gb-devkit#write
Follow the steps for your Operating System (Windows, Mac, or Linux)
We will walk through those steps in class and in the following slides

## Slide 15: Part 1 - Flash the SD Drive
Your kit has a 32 gb SD card. You need to connect that SD card to your host laptop or computer that has internet connectivity. You might need a USB adaptor if your computer does not have an SD card reader
Download the image to your laptop from https://developer.nvidia.com/jetson-nano-2gb-sd-card-image
You do not need to unzip the file
Download Balena Etcher https://www.balena.io/etcher and install.

## Slide 16: Flash the SD Card
Launch the Balena etcher
Select the SD image and then the SD card, then click Flash.
It will take about 10 minutes or so. There will be a graph that tracks the progress and a notice that it is complete when finished. You can remove the card at this point.
For Windows users during the flash, you may get a bunch of pops from Windows that warn you it cannot read the drive. Ignore and close those.

## Slide 17: Part 1 Install SD Card
Install the SD card into your Jetson Nano
Connect the wifi USB adaptor
Connect the USB-C power supply
Connect the Micro-USB cable to the Jetson and your computer
Now we will log in remotely to the Nano using the serial Micro-USB connection to continue setup

## Slide 18: Headless Connection to Nano - Windows
Windows users will need to download and install Putty https://www.chiark.greenend.org.uk/~sgtatham/putty/latest.html
You need to look up the com port in Device Manager (right click windows start icon and select Device Manager).
Look under the Ports(Com and Lpt). You should see something like Com3.

## Slide 19: Headless Connection to Nano - Windows
You need to look up the com port in Device Manager (right click windows start icon and select Device Manager).
Look under the Ports(Com and Lpt). You should see something like USB Serial Device (Com3).
You will need that for Putty

## Slide 20: Headless Connection to Nano - Windows
In Putty, select the ‘Serial’ radio button
Enter COM3 for Serial line and change the speed to 115200
Click on Open

## Slide 21: Headless Connection to Nano - Mac
Use your command prompt to find the serial device
Use the device name to connect:
To terminate press Crtl + a then k, then press y

## Slide 22: Headless Connection to Nano - Windows
You should get a configuration screen. If you get a prompt for a host name, you can reboot the Nano and connect again.
Follow the prompts to accept license agreement and configure.
You should set a username and password.
You can configure your network or do so after configuration is done
You should create the default APP partition file
You should create a 4 GB Swap file

## Slide 23: Part II - Getting Started with Jetson Nano 2GB
Enroll in the course, Getting Started with Jetson Nano, offered by NVIDIA Deep Learning Institute at https://courses.nvidia.com/courses/course-v1:DLI+S-RX-02+V2/
Complete the first section, ‘Setting up your Jetson Nano.’ We will walk through the remaining setup in class and the next few slides
Disregard the instructions referencing the ‘4gb’ version in the NVIDIA Lab instructions.

## Slide 24: Part II
After the initial setup, you should reconnect using wifi or the serial connection
Reconnect using SSH and IP address of serial connection 192.168.55.1 <username>@192.168.55.1
If you have wifi configured but not the IP address, use ifconfig at the command prompt to find it
You need to have wifi enabled to download the docker container

## Slide 25: Common Linux commands
Helpful Cheat sheets:
ubunturef.pdf (cheat-sheets.org)
Linux-Cheat-Sheet-Sponsored-By-Loggly

## Slide 26: Setting up wifi
Reconnect using SSH and IP address of serial connection 192.168.55.1 <username>@192.168.55.1
You can set up wifi from the command line:
  sudo nmcli device wifi connect ‘ssid’ password ‘password’
Use ifconfig to look up IP address (10.0.0.51 is the IP in this image)

## Slide 27: Run docker command
First create a directory:
  mkdir -p ~/nvdli-data
Run the following command to download the container:
  sudo docker pull nvcr.io/nvidia/l4t-ml:r32.6.1-py3
Now run the container (be sure your camera is attached):
  sudo docker run --runtime nvidia -it --rm --network host --volume ~/nvdli-data:/nvdli-nano/data --device /dev/video0 nvcr.io/nvidia/l4t-ml:r32.6.1-py3
You can get these scripts from the NVIDIA container repository at: https://ngc.nvidia.com/catalog/containers/nvidia:dli:dli-nano-ai

## Slide 28: Starting Lab
When the container is launched you should see a message:
Connect to JupyterLab from your host machine’s browser. You s1hould substitute the IP address here with the WiFi address for better performance. 192.168.55.1 uses the mini-usb connection. If we used the IP in slide 26, we would use http://10.0.0.51:8888
Each time you reboot the Jetson Nano, you will need to ssh (wifi should still work) and execute the script to start the Docker Container:
  sudo docker run --runtime nvidia -it --rm --network host --volume ~/nvdli-data:/nvdli-nano/data --device /dev/video0 nvcr.io/nvidia/l4t-ml:r32.6.1-py3

## Slide 29: Connecting to Jetson Nano
SSH using last configured IP
If you need to reconfigure connection, use mini-USB and connect with putty using 192.168.55.1 and serial port
To start network services
    sudo apt update
    sudo apt install network-manager
    sudo service NetworkManager start
To configure IP
  sudo nmcli device wifi connect 'SSID' password 'PASSWORD’

## Slide 30: Check for Disk Space
df

## Slide 31: Containers
Isolate sections of the host Linux Kernel to run software rather then installing a completely separate virtual OS
Docker uses VM in the background to run containers on Windows or Mac machines, runs natively on Linux
Each container has required software libraries and dependencies for running application
Allows for different versions to run
Allows for uniformity across different development machines
Allows for testing of applications across different libraries, build versions, and environments
Reference: The Docker Workshop, PackT Publishing, 2020

## Slide 32: Container Instances
Containers start with an image that is created or downloaded from a repository
The docker run command is used to create an instance of that container
One or more container instances can be run from the same image
Many containers from other images can be run at once

## Slide 33: Check for container images
List running containers:
docker container ls -a
Stop running containers
docker container stop [container_id]
remove a stopped container
docker container rm [container_id]
remove all stopped docker containers
docker container rm $(docker container ls –aq)
to wipe docker clean and start from scratch
docker container stop $(docker container ls –aq) && docker system prune –af ––volumes
list docker images:
docker image ls

## Slide 34: Remove Container Images
list docker images:
docker image ls
make note of image id and remove docker image
docker image rm [image_id1] [image_id2]
docker image rm bc9051ff252d

## Slide 35: Pull NVIDIA image with common DL framework
NVIDIA L4T ML | NVIDIA NGC https://ngc.nvidia.com/catalog/containers/nvidia:l4t-ml
pull command docker :
  nvcr.io/nvidia/l4t-ml:r32.5.0-py3
Run Command:
  sudo docker run -it --rm --runtime nvidia --network host nvcr.io/nvidia/l4t-ml:r32.5.0-py3
Note that the default password used to login to JupyterLab is nvidia.
Notes: #revise to add parameters, add slide on containers

## Slide 36: Jupyter Lab
Navigate to Jupyter Lab once the container is run
Remember that is the assigned IP:8888

## Slide 37: Upload Code
Create a folder to hold code that you will upload
Upload a zip file of the code to your computer
Start a Notebook and add this code to unzip the file (modify to your file):
  #unzip dataset and extract to data directory
  import zipfile as zf
  files = zf.ZipFile("computervision.zip", 'r')
  files.extractall('computerv/')
  files.close()

## Slide 38: Code from Github
Launch terminal
Make sure you are in nvdli-nano directory, type this at terminal:
cd nvdli-nano
Now clone git repository into directory:
git clone https://github.com/pattydelafuente/jetsonclass.git
You should see a folder created in nvdli-nano with the name of the repository which in this case is jetsonclass.

## Slide 39: Explore
Test out the code
You may have to install libraries
Remember that for speech, you will need to connect a usb headset directly to your nano
For video files, you may need to modify the code for the camera – refer to the Getting Started with Jetson lab for working with the camera on the jetson

## Slide 40
Thank You
Edge AI and Robotics Teaching Kit