## Slide 1: Lecture 1.5 Edge, AIoT, Big Data
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
Big Data
Edge & Embedded Computing
IOT/ Cloud

## Slide 4: Learning Objectives
Differentiate between Edge, Embedded, Cloud and On-Premise.
Describe Big Data and Distributed Computing
List the pros and cons of AIOT computing
List common applications of Aiot Computing

## Slide 5: Big Data

## Slide 6: The 5 Vs of Big Data
Every minute:
  more than 300,000 tweets are created
  Netflix subscribers are streaming more than 70,000 hours of video at once
  Apple users download 30,000 apps
  Instagram users like almost two million photos
Big Data encompasses both structured and highly unstructured forms of data
© Cambridge University Press 2018

## Slide 7: The 5 Vs of Big Data
Volume: the amount of data, also referred to the data “at rest”
Velocity: the speed at which data comes in and goes out, data “in motion”
Variety: the range of data types and sources that are used, data in its “many forms”
Veracity: the uncertainty of the data; data “in doubt”
Value: TCO and ROI of the data
© Cambridge University Press 2018

## Slide 8: The 5 Vs of Big Data
Examples:
  Large-scale enterprise systems (e.g., ERP, CRM, SCM)
  Social networks (e.g., Twitter, Weibo, WeChat)
  Internet of Things
  Open data
© Cambridge University Press 2018

## Slide 9: Big Data Storage
Schema on Read, rather than Schema on Write
  Schema on Write – preexisting data model, how traditional databases are designed (relational databases)
  Schema on Read – data model determined later, depends on how you want to use it (XML, JSON)
  Capture and store the data, and worry about how you want to use it later
Data Lake
  A large integrated repository for internal and external data that does not follow a predefined schema
  Capture everything, dive in anywhere, flexible access
Copyright © 2019, 2016, 2013 Pearson Education, Inc. All Rights Reserved

## Slide 10: Infrastructure Advances in Data Management
Massively parallel processing (MPP)
  divide a computing task (such as query processing) between multiple processors, speeding it up significantly
In-memory DBMS
  keep the entire database in primary memory, thus enabling significantly faster processing
In-database analytics
  no need to move large quantities of data to separate analytics tools for processing
Columnar DBMS
  reorient the data in the storage structures, leading to efficiencies in data warehousing and analytics applications
Copyright © 2019, 2016, 2013 Pearson Education, Inc. All Rights Reserved

## Slide 11: Hadoop
Open-source software framework used for distributed storage and processing of big datasets
Can be set up over a cluster of computers built from normal, commodity hardware
Many vendors offer their implementation of a Hadoop stack (e.g., Amazon, Cloudera, Dell, Oracle, IBM, Microsoft)
© Cambridge University Press 2018

## Slide 12: History of Hadoop
Key building blocks:
  Google File System: a file system that could be easily distributed across commodity hardware, while providing fault tolerance
  Google MapReduce: a programming paradigm to write programs that can be automatically parallelized and executed across a cluster of different computers
Nutch web crawler prototype developed by Doug Cutting
  Later renamed to Hadoop
In 2008, Yahoo! open-sourced Hadoop as “Apache Hadoop”
© Cambridge University Press 2018

## Slide 13: Data/Compute Infrastructure

## Slide 14: Data and Compute Infrastructures
On-Premise Data is located within your local network but could be in a central location within that network
Cloud – Data is external to your network and accessed over HTTP
Embedded / Edge – Process Data closer to source rather than a remote or central location

## Slide 15: On-Premise Datacenter
https://www.cisco.com/c/en/us/td/docs/solutions/Enterprise/Data_Center/DC_Infra2_5/DCInfra_1.html

## Slide 16
This Photo by Unknown Author is licensed under CC BY

## Slide 18: Embedded and Edge Computing

## Slide 19
LATENCY
BANDWIDTH
CONNECTIVITY
1 billion+ cameras worldwide
10’s of petabytes per day
Safety-critical services
Realtime decisions
50% of populated world < 8mbps
Bulk of uninhabited world no 3G+
PRIVACY
Data Redaction + Confidentiality
Private cloud or on-premises storage
PRIVACY
WHY AI AT THE EDGE
Notes: Why is AI at the edge so important? It’s simple – for systems in the field, there are many use cases where you simply cannot rely on a round trip through the cloud to solve the problem. For some problems like AI Cities the scale is so big and the amount of data generated is so vast that the network cannot possibly support it. For robotics you have devices that support safety-critical services and need to make millisecond decisions at the speed of light.
For many companies data security is of paramount importance, to protect the privacy of individuals and to keep intellectual property safe. And for many applications in remote areas where robots and UAVs are ideally suited, network coverage is spotty or just doesn’t exist, or is slower with the degraded speeds of 2G or satellite communications. Relying on the cloud may not be an option when the connection isn’t always available.
If you want to solve these problems with AI you must have decision-making At the edge. That’s at the camera, on the robot, in the drone. But the past there was never a platform that could do this. How do you get the kind of supercomputing performance you need to do inferencing on large and deep neural networks in the power envelope and size constraints at the edge? Enter NVIDIA’s Jetson embedded computing platform.

## Slide 20: THE JETSON FAMILY
for AI at the Edge and Autonomous System designs
Multiple modules - Same software
Full specs at developer.nvidia.com/jetson
7.5 – 15W
45mm x 70mm
JETSON TX2 NX
1.3 TFLOPS (FP16)
5 - 10W
45mm x 70mm
JETSON NANO
0.5 TFLOPS (FP16)
10 – 30W
100mm x 87mm
JETSON AGX XAVIER series
11 TFLOPS (FP16)
32 TOPS (INT8)
10 - 15W
45mm x 70mm
JETSON XAVIER NX
6 TFLOPS (FP16)
21 TOPS (INT8)
AI at the edge
Fully autonomous machines

## Slide 21: Data Latency by Distance
Distance from Server to User | Network Latency | Typical Packet Loss | Throughput / Quality
Local < 100 miles | 1.6 MS | 0.6% | 44 Mbps (UDHTV)
Regional 500 – 1000 miles | 16 MS | 0.7% | 4 Mbps (sub DVD)
Average RTS (US) | 72 MS | 1% | 1.62 Mbps (sub TV)
Average RTS (Global) | 94 MS | 3% | 1.2 MS (poor)
Notes: 4 concerns: latency, bandwidth, security, ?

## Slide 22
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 23: Embedded/ Edge Computing
Compute, controller and AI commands are local to machine
Use cases include Robotics, smart machines, self driving cars
Often units are mobile requiring power supply
Trades offs between computing power, power consumption, data storage and weight
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 24: Internet of Things / Cloud Computing

## Slide 25: Internet of Things (IoT)
Accessing data and services over Internet. AIoT refers to Artificial Intelligence Internet of Things

## Slide 26: AIoT Applications
Fitness Applications
Smart Home
Siri and Google Assistant
Doorbell Cameras
Voice Services
Machine Learning Models such as ImageNet
Phone Number Spoofing Applications

## Slide 27: AIoT
Pros
Instant Access
Leverage existing work on AI Models (imagine if you built an image library on your own and had to initially hand label training data)
Reduce compute resources and power consumption
Cons Services not available without Internet
Recurring subscription or monthly costs
Latency

## Slide 28: Cloud Services
On demand and instant access of compute and software resources
Reduces need for IT Hardware administration and resources
Has recurring monthly cost
Depending on resources used, requires skilled IT Server resources referred to as DevOps Administrators and Engineers
Learning curve and training required to setup and administer different compute resources when moving between cloud vendors

## Slide 29: Cloud Compute and GPU Services
Cloud Vendor | Services | Cost
Microsoft Azure | Cloud Services: https://azure.microsoft.com/en-us/ GPU Instances: https://docs.microsoft.com/en-us/azure/virtual-machines/sizes-gpu | Cost estimate: https://azure.microsoft.com/en-us/pricing/calculator/
Amazon Webservices | Cloud: https://aws.amazon.com/products/compute/?nc2=h_ql_prod_cp GPU: https://docs.aws.amazon.com/dlami/latest/devguide/gpu.html | https://aws.amazon.com/pricing/
Google | Google Cloud: https://cloud.google.com/gpu/#section-4 Colab: https://colab.research.google.com/ | https://cloud.google.com/compute/gpus-pricing

## Slide 30
Thank You
Edge AI and Robotics Teaching Kit