## Slide 1: Lecture 1.8 Computer Vision
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
Introduction
How a computer sees an image
OpenCV
PyCuda
OpenCV CUDA
Working with Videos
Working with a Webcam

## Slide 4: Introduction
This module introduces you to the basics of working with images and videos using OpenCV, PyCuda and OpenCV CUDA

## Slide 5: Computer Vision
Computer vision is the task of understanding the images captured by a camera
Vision tasks that are simple for humans to do, can be very difficult for a computer
  For example, color each fruit a different color
Notes: Computer vision, also known as machine vision, is the job of creating program and algorithms to extract useful information about images captured by a camera
For a robot, this could be distinguishing what areas around it are occupied by obstacles or recognizing which person is nearby
These tasks can often seem very simple and easy for humans, but to write a program to accomplish such tasks can be very difficult
Computers do not inherently have the years of visual experience nor the tactile experiential knowledge that humans have
Without a model of the world, determining the content of an image can be quite challenging

## Slide 6: Learning Objectives
Describe how computers see images
Work with OpenCV utilities to read, write and transform images and videos
Demonstrate ability to leverage GPU enabled libraries to process images

## Slide 7: Image Processing
Images are made up of a bunch of pixels. Each pixel has attributes such as location, color, and distance to other pixels.
There are numerous methods to display images in Python.
OpenCV for Python is an opensource library popular in the Machine Learning community. More info can be found at https://pypi.org/project/opencv-python/. Images in OpenCV are primarily numpy arrays.
OpenCV can be combined with PyCuda, Tensorflow and other GPU enable tools to improve processing
How a computer sees an image

## Slide 8: Images and Image Representation
Camera images are 2-dimensional arrays of pixels
  Each pixel is a ‘picture element’
  Resolution is the width x height (e.g. 640x480, 1024x768)
Another image statistic is the number of pixels used to represent the image
  1 megapixel or 2 megapixels
  The higher the resolution, the more information available, but it takes more time to processes higher resolution images
Notes: An image captured by a camera is a 2-dimensional array of pixels
Pixels are discretized picture elements which when put together form the original image
The higher the resolution, the more visual detail is captured in the image, but it does take more time to process a higher resolution image
The image captured by the Jet camera is 640x480, which is .3 megapixels. Even this resolution can take some time to process, so sometimes it is necessary to convert the image to a lower resolution.

## Slide 9: Binary Images and Grayscale
Grayscale image have each pixel representing a single intensity value
  A value of 0 is black (lowest intensity)
  A value of 255 is white (highest intensity)
  128 is the midpoint and can be used as a threshold for pixel intensity
  These images look like a typical black and white image
  Average the RGB values to convert color to grayscale
Binary images have each pixel either on (1) or off (0)
  These images are useful as an intermediate representation for other operations
Notes: Grayscale image are what we typically think of as black and white images
The difference here is that the color components are represented as a single value. For example, this could be a single 8-bit value
0 is black and 255 is white.
Converting a color image to grayscale is done by averaging the 3 color channels.
When color is not needed, these images can be faster to process.
Binary images are images where the pixel value is a 1 or a 0.
These images can be useful intermediate representations when detecting edges or lines.

## Slide 10: Generate a Grayscale image - CPU
Generating, writing and reading a random grayscale image

## Slide 11: Color Images
Color images can be represented with 3 values per pixel
  A common representation is RGB (Red, Green, Blue)
  Each color value is an 8-bit number between 0 and 255
  Black is all 3 values being 0
  White is all 3 values being 255
  To represent this type of image, there are 3 parallel 2-D arrays
    One 2-D array for each color
Notes: Color images are represented as 3 values per pixel
A common representation has 3 bytes for each pixel and each byte represents the Red, Green, and Blue components of the pixel color
Each color component can then be represented as a value from 0 to 255
This is often called 24-bit color (3 x 8 bits)
Brighter colors will have higher component values. White is all 3 values being 255. Black is all 3 values being 0.
For example, a 640x480 image will take 921,600 bytes (640*480*3 = 921,600)

## Slide 12: Generate a Color Image - CPU
Generating, writing, and reading a random color image

## Slide 13: Example Open CV Code to Read an Image - CPU
import cv2
import numpy as np
import os
from IPython.display import display
from PIL import Image
img3 = cv2.imread('images/aqualung.jpg')
display(Image.fromarray(img3))
Reading and display Image

## Slide 14: OpenCV for Python
Opensource Computer Vision (OpenCV) -popular opensource library for working with and displaying images and videos https://docs.opencv.org/4.5.3/d1/dfb/intro.html
OpenCV can be used with other libraries such as PyCuda to GPU enable image processing.
Some of the OpenCV functions are CUDA enabled gpu. GPU-accelerated Computer Vision — OpenCV 2.4.13.7 documentation . Good reference for getting started OpenCV Cuda: Getting Started with OpenCV CUDA Module | LearnOpenCV

## Slide 15: OpenCV with PyCuda
#pass c code to perform work on GPU
mod = SourceModule \
(
'''
#include<stdio.h>
#define INDEX(a, b) a*256+b
__global__ void bgr2gray(float *d_result,float *b_img, float *g_img, float *r_img)
{
unsigned int idx = threadIdx.x+(blockIdx.x*(blockDim.x*blockDim.y));
unsigned int a = idx/256;
unsigned int b = idx%256;
d_result[INDEX(a, b)] = (0.299*r_img[INDEX(a, b)]+0.587*g_img[INDEX(a, b)]+0.114*b_img[INDEX(a, b)]);
}
''' )
PyCuda integrates with Python by using SourceModule to pass through C code:

## Slide 16: OpenCv with PyCuda
h_img = cv2.imread('lena_color.tif',1)
r_img = h_img[:, :, 2].reshape(65536).astype(np.float32)
h_result=r_img
#create instance of cuda function
bgr2gray = mod.get_function("bgr2gray")
#call pycuda function and output image
bgr2gray(drv.Out(h_result), drv.In(b_img), drv.In(g_img),drv.In(r_img),block=(1024, 1, 1), grid=(64, 1, 1))
h_result=np.reshape(h_result,(256,256)).astype(np.uint8)
#display transformed image
image_widget = ipywidgets.Image(format='jpeg')
image_widget.value = bgr8_to_jpeg(h_result)
display(image_widget)
#original image
orgimage_widget = ipywidgets.Image(format='jpeg')
orgimage_widget.value = bgr8_to_jpeg(h_img)
display(orgimage_widget)
Create instance of and use function created in previous slide

## Slide 17: OpenCV for CUDA
Some OpenCV image libraries are CUDA enabled which simplifies working with the GPU
Typical steps to work with OpenCV CUDA:
  Import libraries
  Upload image to GPU Device
  Perform image processing
  Download image back to CPU
  Display image

## Slide 18: Let’s compare coding for CPU vs GPU
#CPU version
img = cv2.imread("images/statue_small.jpg", cv2.IMREAD_GRAYSCALE)
#contrast Limited Adaptive Histogram Equalization
clahe = cv2.createCLAHE(clipLimit=5.0, tileGridSize=(8, 8))
imgr = clahe.apply(img)
plt.subplot(121)
plt.imshow(imgr)
plt.title("cpu clahe")
plt.xticks([])
plt.yticks([])
plt.show()
This calls the OpenCV CLAHE transformation – CPU Version

## Slide 19: Let’s compare coding for CPU vs GPU
#reference https://learnopencv.com/getting-started-opencv-cuda-module/
img = cv2.imread("images/statue_small.jpg", cv2.IMREAD_GRAYSCALE)
src = cv2.cuda_GpuMat()
src.upload(img)
clahe = cv2.cuda.createCLAHE(clipLimit=5.0, tileGridSize=(8, 8))
dst = clahe.apply(src, cv2.cuda_Stream.Null())
result = dst.download()
#cv2.imshow("result", result)
#cv2.waitKey(0)
plt.subplot(121)
plt.imshow(result)
plt.title("cuda clahe")
plt.xticks([])
plt.yticks([])
plt.show()
This calls the OpenCV CLAHE transformation – CUDA GPU Version

## Slide 20: Working with Videos
You can directly read and display a video file using ipywidgets:
from IPython.display import display
from ipywidgets import Video, Image
import numpy as np
import base64
video = Video.from_file('hallway.mp4')
video

## Slide 21: Transforming Videos
Build upon what you learned when working with Images
Reading in video
Loop through each frame (image)
Apply transformation to each fram
Append frame to new video
Steps

## Slide 22: Working with Videos - OpenCV
Import cv2
cap = cv2.VideoCapture('hallway.mp4')
frames = []
while(1):
try:
_, frame = cap.read()
fgmask = cv2.Canny(frame, 100, 100)
mask = fgmask > 100
frame[mask, :] = 0
frames.append(frame)
except Exception:
break
You will want to use OpenCV to perform transformations – each video frame is an image
width = int(cap.get(3))
height = int(cap.get(4))
filename = 'output.mp4'
fourcc = cv2.VideoWriter_fourcc(*'avc1')
writer = cv2.VideoWriter(filename, fourcc, 25, (width, height))
for frame in frames:
writer.write(frame)
cap.release()
writer.release()
with open(filename, 'rb') as f:
video.value = f.read()

## Slide 23: Working with your Camera
You use the video capture function and pass in a 0 other number to represent your webcam.
cap = cv2.VideoCapture(0)
If you have just one camera, it is usually device 0. If you have both a webcam and USB, the USB might be assigned a 1.
To see if a webcam is abled on your nano, you can run:
  !ls -ltrh /dev/video*
Sample results:

## Slide 24: Possible Camera Errors with Nano
Common Camera errors:
Your camera is not connected
For remote containers, you did not add the parameter to attach your device. Stop the container and run again with the required parameter to attach your camera:
  E.G. sudo docker run --runtime nvidia -it --rm --network host --device /dev/video0 dustynv/l4t-ml:r32.5.0-py3
If this is a windows machine, typically your primary camera will be device 0 (e.g. cv2.VideoCapture(0) ) but if it is a USB camera and you have an embedded camera, it may be device 1. You can always set the value in the USBcamera class to cv.VideoCapture(1) and test it out.
Troubleshooting

## Slide 25: Summary
This module covered:
how images are represented computationally
How to work with images and videos using OpenCV
How to integrate use of GPUs with OpenCV using PyCuda and OpenCV CUDA
How to work read in images from a connected webcam

## Slide 26
Thank You
Edge AI and Robotics Teaching Kit