## Slide 1: Lecture 4.2 Teaching Machines to Act
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
Components
JetBot Assembly
JetBot Configuration
Controlling Motors

## Slide 4: Learning Objectives
The JetBot’s role as the intelligent agent
List the components needed build and program robots
Connect motors and microcontrollers to Jetson Nano
Discuss how to connect sensors to the microcontrollers and embedded computers
Execute sample code for jetson to control motors and read camera data

## Slide 5: JetBot
The JetBot used in this curriculum is serving as the Intelligent Agent
By collecting data, we can train machine learning models to learn based on past experiences such as if an object is considered an obstacle or not

## Slide 6: JetBot (Original and Waveshare)
CONTROLLER：Jetson Nano 2GB
OS：Ubuntu 18.04 LTS
CAMERA：8MP HD resolution, 160° FOV wide angle camera
OLED：0.91" 128×32 pixels
2.4GHz / 5.8GHz dual-band WiFi
TELEOPERATION：Gamepad, webpage
DRIVING TYPE：Differential 2WD
POWER SUPPLY：12.6V, 18650 battery × 3(connected in series)（Note: the 18650 batteries are NOT included.）
MOTOR：TT motor,Reduction rate 1:48,Idle speed 240RPM
CHASSIS: Aluminum alloy chassis

## Slide 7: JetBot
Two wheeled differential drive robot
Features and embedded Jetson Nano to enabled advanced GPU deep learning in a power efficient form
Notes: Uses Jetson Nano 2GB or 4gb
OS：Ubuntu 18.04 LTS or higher
CAMERA：8MP HD resolution, 160° FOV wide angle camera
OLED：0.91" 128×32 pixels
2.4GHz / 5.8GHz dual-band WiFi
TELEOPERATION：Gamepad, webpage
DRIVING TYPE：Differential 2WD – does not use steering. Direction is controlled by movement of the motors with. Some kits use a castor ball for balance
POWER SUPPLY：12.6V, 18650 battery × 3(connected in series)（Note: the 18650 batteries are NOT included.）
MOTOR：TT motor, Reduction rate 1:48,Idle speed 240RPM
CHASSIS:Aluminum alloy chassis

## Slide 8: Components Needed

## Slide 9: JetBot Components for Navigation
Motors
Motor Controller
Power
Jetson Nano
Programming Framework

## Slide 10: JetBot – Example Hardware List
Metal box
Camera holder
Acrylic camera spacer
IMX219-160 Camera
USB WiFi
JetBot expansion board
Motor x2
Wheel x2
Caster x2
Power adapter EU head
12.6V battery charger
Wireless gamepad
Screwdriver x2
6pin 9cm cable
Screws pack
4010 cooling fan
Micro SD card reader

## Slide 11: Jetbot Starter Kits from 3rd Party Vendors
Sparkfun 2GB Jetbot AI Kit (includes Jetson 2GB Nano) https://www.sparkfun.com/products/17246?_ga=2.207276947.1825498701.1618365011-547466400.1618365011
Waveshare 2GB Jetbot kit - https://www.waveshare.com/product/ai/boards-kits/jetson-nano/jetbot-2gb-ai-kit.htm?sku=18984
Assembly Instructions: http://jetbot.org/v0.4.3/getting_started.html

## Slide 12: Machine Components
Motors convert electrical energy into mechanical energy (rotation)
Higher voltage increase motor speed and torque
Most JetBot kits use TT DC motors which do not have encoders and speed will depend on voltage, load and resistance
More advanced DC motors use Encoders which measure distance and speed to determine position and location
are used to measure the distance travelled by the robot
encoder values are published to ROS topics
Motors
Notes: Motor convert electrical energy which is applied from the battery and converts that into rotational mechanical energy
There are 2 DC – 2 pin motors on the JetBot, each drives one of the wheels

## Slide 13: Motor Pinout
The Jet TT motors have a 2-pin connector with voltage of 3vdc to 6vdc
Motors are directly connected to a board to regulate power and drive motors
Notes: This Jetbot is a slight variation in that the motor driver is not on an expansion board but this image gives a better illustration of what is required to integrate mobility with a Jetson Nano
The motor connector on the Jetbot is a 2-pin header
The pins should be connected to a motor board that drives the motor and regulates power.

## Slide 14: JetBot Starter Code
Some of the kits come with an SD card preloaded with the Operating System and JetBot starter Jupyter Notebooks.
You can flash your own SD card and use the preloaded notebooks or run the container. Instructions can be found at: https://jetbot.org/master/software_setup/sd_card.html
Use this image in place of the other SD image for the jetson. You will need to configure the Operating System on first boot and Wi-Fi prior to remote connectivity with a browser to access the Jupyter Notebooks.
Alternatively, you can use the same SD image for Getting Started with AI but run a different docker container: https://jetbot.org/master/software_setup/docker.html
Note that these images and container use Jetpack L4.4.

## Slide 15: Lab – Controlling Your Jetson
The JetBot images and container contains code out of the box that demonstrates controlling your JetBot.
Work through the Basic Motion Jupyter Notebook to perform simple commands to move your JetBot.
You can also view the Jupyter Notebook from the Github website at https://github.com/NVIDIA-AI-IOT/jetbot/blob/master/notebooks/basic_motion/basic_motion.ipynb.

## Slide 16
Thank You
Edge AI and Robotics Teaching Kit