## Slide 1: Lecture 4.3 Introduction to ROS2
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
Why ROS2
Installing ROS2
Getting Started with ROS2
ROS2 Commands
Robot Simulators
Gazebo
4.3 Intro to ROS

## Slide 4: ROS2
Robot Operating System

## Slide 5: Why ROS2
The starter code with using Jupyter Lab and Jupyter Notebooks are a great way to get familiar with programming and training deep learning models with the Jetson Nano powered JetBot AI kits
In production environments, ROS provides greater control and flexibility for automating robotic processes.
Official documentation for ROS2 can be found at http://docs.ros.org/en/rolling/ .

## Slide 6: Jetbot_Ros
A github project at
https://github.com/dusty-nv/jetbot_ros
Provides source code and containers with ROS and Gazebo libraries ready to go
Can use against physical JetBot or virtual (using Gazebo plugin)
Easy to use containers with ROS2 and Gazebo

## Slide 7: ROS and ROS 2
https://www.ros.org/
Open source, meta-operating system for robots, ideal for multiple sensors
Distributed framework in that different processes can be run on different machines
Compatible with C++, Python, and Lisp
ROS1 and ROS2 versions (pay attention to version that is compatible with your operating system and robot you are building)
ROS2 has a version for Windows and Mac

## Slide 8: ROS 2 – Key concepts
Nodes – controls one key function (e.g., sensor reading, motors, etc) and can send and receive info
Topics – Nodes use a Publisher subscriber model to exchange data
Services – Method of communication to provide data when requested by client
Parameters – Configurable values of node settings
Actions – Action client can send a send a goal to an action server and receive the result of that goal. Leverages the Topic/Service nodes.

## Slide 9: Install – ROS 2 and Gazebo
dusty-nv/jetbot_ros: ROS nodes and Gazebo model for NVIDIA JetBot with Jetson Nano (github.com)
SSH into your Jetson and at the terminal, first clone this github:
  git clone https://github.com/dusty-nv/jetbot_ros
  cd jetbot_ros
  docker/run.sh
If you have a Jetson Nano but not the whole JetBot kit, you can still follow along by using Gazebo work with a virtual Jetbot.
The container has ROS2 and Gazebo installed.
Build and Install Docker Container
git clone https://github.com/dusty-nv/jetbot_ros cd jetbot_ros docker/run.sh

## Slide 10: ROS2
ROS2 is a distributed framework that allows easy and rapid robot software development
ROS2 itself runs on top of Linux and provides
  Package management
  Message passing between running programs
  Drivers for different hardware
New ROS2 packages can be easily installed into a system
Robot Operating System 2

## Slide 11: ROS2 Nodes
Nodes are process that are performing some computation
You can think of a ROS node as a running program that can read values from other nodes and also send out values
The intelligent agent can be directed to perform an action based on values
Notes: Nodes are processes that perform some computation. A node may be managing reading a sensor or reading camera images. Another node may be used to control the motors.

## Slide 12: ROS2 Topics
Topics are the named communication channels between nodes
Example topics on JetBot
  /left_motor (controls the left motor)
  /right_motor (controls the right motor)
  /image_raw (the image from the camera)
Notes: Topics are named channels for communicating messages between nodes. Naming convention begins with a forward slash.
A node can periodically publish sensor data to a topic
Several other nodes can subscribe to that topic to receive the sensor data
Topics are strongly typed. That means that messages published to a topic need to match the message type for that topic.
Publishers and subscribers are not aware of each other when using topics

## Slide 13: ROS2 Services
Services are procedures that answer requests.
Services are like functions in a programming language.
Example services on JetBot
  /data_recorder/save_image (saves the current camera image)
  /data_recorder/start_recording (records the camera feed to a video file)
Notes: Services are ways of requesting and receiving results.
A node can make a service request to another node that advertised the service.
Services are given a name (like topics)
Services have request type and a response type.

## Slide 14: ROS2 Parameters
Parameters are variables that store settings in ROS
Example parameters on JetBot
  /cv_camera/image_width (width in pixels of camera image)
  /motor_control/maxspeed (maximum speed of the motors
Notes: Parameters are used to store configuration details
Parameters have names that follow the same conventions as topics
Parameters are often set at startup and remain unchanged

## Slide 15: Useful ROS2 Commands
Commands for building source code
  colcon build (or catkin make for ROS)
ros2 run
  Launches an executable to create a node
  ros2 run <packagename> <executable name>
ros2 topic
  ros2 topic echo
  ros2 topic list
ros2 service
  ros2 service list
  ros2 service call
ros2 launch: can be used to launch multiple nodes

## Slide 16: ROS2 Launch
E.G. sample command and file ros2 launch jetbot_ros teleop_keyboard:
import os
from launch import LaunchDescription
from launch.actions import IncludeLaunchDescription
from launch.launch_description_sources import PythonLaunchDescriptionSource
from launch.substitutions import ThisLaunchFileDir,LaunchConfiguration
from launch_ros.actions import Node
def generate_launch_description():
teleop_keyboard = Node(package='jetbot_ros', node_executable='teleop_keyboard',
prefix='lxterminal -e', #'xterm -e'
output='screen',
emulate_tty=True)
return LaunchDescription([
teleop_keyboard
])
ros2 launch executes a python file that configures and starts one or more nodes
Notes: Ros2 launch files can specify many nodes with many parameters
Ros2 launch files can “include” other ros2 launch files

## Slide 17: Creating ROS2 Software
ROS2 nodes can be written in Python or C++
Catkin was the preferred build tool for earlier ROS nodes.
  # ROS Melodic
  $ catkin_make
  $ source devel/setup.bash
ROS2 uses Colcon build
  # ROS2 Foxy
  $ colcon build
  $ source install/local_setup.bash

## Slide 18: ROS2 Development
Used to build a ROS 2 workspace
For more info: https://docs.ros.org/en/foxy/Tutorials/Colcon-Tutorial.html
Install on Linux: sudo apt install python3-colcon-common-extensions
Create workspace directory with subdirectory called src:
  mkdir -p ~/ros2_ws/src
  cd ~/ros2_ws
Add source files or clone source files
Source your setup file for every new terminal window opened:
  ~/ros2_foxy/install/local_setup.bash
Colcon Build Instructions

## Slide 19: ROS2 and Jetson Nano
To launch JetBot and start motors:
  ros2 launch jetbot_ros jetbot_nvidia.launch.py
To launch virtual JetBot using Gazebo
  ros2 launch jetbot_ros gazebo_world.launch.py
Then open another terminal window, navigate into the container:
  sudo docker exec -it jetbot_ros /bin/bash
To launch keyboard control to manually drive JetBot
  ros2 launch jetbot_ros teleop_keyboard.launch.py
Using Jetbot_ros container
sudo docker exec -it jetbot_ros /bin/bash

## Slide 20: Robot Simulators
Virtual Robot Environment

## Slide 21: Virtual Environment
It’s not always convenient or cost effect to develop and test directly on the robots
Robot Simulators is software that enables developers to model physics and interactions of virtual robots within a virtual environment
Can build code using virtual environment and then test against the real thing

## Slide 22: Module 4 Lab – Launch Virtual Jetbot
See lab for this exercise or access the Jetbot_Ros project on Github at https://github.com/dusty-nv/jetbot_ros

## Slide 23: Robot Simulation Tools
Gazebo (gazebosim.org) is well known simulator in the opensource community
NVIDIA Isaac Sim https://developer.nvidia.com/isaac-sim is a robotic simulator powered by NVIDIA Omniverse to enable enterprise robotic similations at scale
NVIDIA Omniverse https://www.nvidia.com/en-us/omniverse/ provides an open platform for virtual collaboration and realtime accurate physical simulation

## Slide 24: Gazebo
Included as an add on and integrated with ROS
Also available as standalone install http://gazebosim.org/
Can create a model for any real-world robot to build and test against it in a simulated environment
Additional information on working with integrated ROS2 and Gazebo can be found at http://gazebosim.org/tutorials?tut=ros2_installing&cat=connect_ros#TestingGazeboandROS2integration
A virtual JetBot model and sample worlds can be found at https://github.com/dusty-nv/jetbot_ros/tree/master/gazebo

## Slide 25
Thank You
Edge AI and Robotics Teaching Kit