## Slide 1: Lecture 4.4 Robot Navigation
Edge AI and Robotics Teaching Kit

## Slide 2
The Edge AI and Robotics Teaching Kit is licensed by NVIDIA and UMBC under the
Creative Commons Attribution-NonCommercial 4.0 International License.

## Slide 3: Topics
List the components involved in Robot Navigation
Describe and demonstrate using camera images to perform Robot Navigation
Describe what Mapping is and how it is essential to Robot navigation
Describe other methods for position and path planning
Demonstrate integration of basic robot navigation and collision python

## Slide 4: Robot Navigation

## Slide 5: JetBot Components for Navigation
Motors
Motor Controller
Camera
Power
Jetson Nano
Deep Learning Programming Framework

## Slide 6: Navigation Methods
You can make use of the Jetson Nano GPU, NVIDIA’s CUDA Deep Learning framework and camera to provide sophisticated autonomous navigation capabilities.
Jetson uses camera images to determine obstacles and path forward
Certain use cases such as drones will need more than a camera for navigation. You upgrade from the basic JetBot hardware to include Lidar and other sensors that provide more advanced Location and Mapping capabilities. We will mention some of those methods, but they are beyond the scope of this Teaching Kit.

## Slide 7: Steps for Navigation and Obstacle Avoidance - Jetbot
The JetBot starter notebooks provide exercises to perform the four required steps which are:
Collect data on free and blocked paths
Train a classification model using Pytorch and a Neural Network such as Resnet-18
Optimize the Model using TensorRT
Load the model and demonstrate

## Slide 8: Mapping

## Slide 9: Mapping in Robotics
Maps are essential for robots to devise plans for navigating
Robots use maps to avoid obstacles and find shortest paths
Often robots update their own maps as they explore and learn
Notes: Robots can use maps for planning, but maps can also be used by external parties to instruct fleets of robots on how to navigate
It is imperative that robots do not rely solely on maps because most environments are dynamic and the map may not perfectly reflect the environment.

## Slide 10: Aerial Maps
A top-down view of an environment provides useful information that may be impossible to gather by a ground robot
Sources of aerial maps
  satellites
  drones
  planes
Notes: Aerial maps are the most common type of map used by humans for navigation.
Common tools for navigating like TomTom, Google Maps, and Bing Maps all use aerial data from planes and satellites
Satellite maps are usually only useful to an accuracy of a couple meters, so local maps and sensors are used for avoiding small obstacles and local planning.

## Slide 11: Point Clouds
Point Clouds or a set of coordinate with x,y,z values
Sometimes points will also have color data associated with them.
http://grail.cs.washington.edu/rome/dense.html
Notes: Point clouds are one of the most common ways of building maps for robotics.
Dense point clouds provide more information but they can require more computing power to process
Point clouds can be used to render 3D mesh models that require less space to store and are easier for robots to navigate around.

## Slide 12: Generating Point Clouds
Stereo Cameras
LiDAR
Radar
Structure From Motion
Image Alignment and Stitching
Notes: Point clouds can be produced by a number of different sensors and techniques
Stereo cameras use two overlapping camera views to reconstruct depth data to produce point clouds
LiDAR and radar produce high density point clouds by capturing depth data continuously.
Even a monocular camera can be used to gather depth information by moving the camera and running algorithms that use the motion information to combine the images into depth information
A large number of independent images can be combined to estimate depth and produce point clouds (like the coliseum in the previous slide).

## Slide 13: Other Path Planning Methods

## Slide 14: Simultaneous Localization and Mapping
JetBot does not use SLAM
SLAM is used by robots that must construct a map of their environment while localizing themselves
SLAM is used by self-driving cars, agricultural robots, and underwater robots
GPS can be used to aide SLAM, but GPS alone is insufficient for SLAM.
Notes: Jetson does not use SLAM due to storage and bandwidth. It primarily relies on Camera image vectors for searches and mapping.
Robots use SLAM to refine and update the data in provided maps
SLAM is useful when a robot does not have a perfect map of its environment.
SLAM is made more challenging when the environment is dynamic and there are other moving entities.
Typically SLAM solutions rely on LiDAR or stereo cameras but solutions exist when only radar, sonar, or tactile sensors are available.

## Slide 15: Solution Likelihood
SLAM operates by maximizing two likelihoods:
  likelihood of the map given the pose and sensor readings of the robot
  likelihood of the pose of the robot given the map and the sensor readings
Simultaneously optimizing for both of these will let the robot produce a map while estimating its pose in the map
Notes: Landmarks are used to assess likelihood. If a robot is near a landmark according to its sensors and it is near that same landmark in the map then the map and its pose are both likely
Choosing the correct landmarks is a critical task that is essential to robustly maximizing the map and pose likelihoods.

## Slide 16: Kalman Filters
Extended Kalman Filters can be used to estimate the pose of the robot and the map
The state vector is the landmarks and the pose of the robot
The map transforms are non-linear so the basic Kalman Filter is insufficient
Complexity is quadratic with number of landmarks
Notes: Kalman filters are a straightforward way to implement SLAM because adding the landmarks is a simple extension to the Kalman filter that we used in the dead-reckoning module
The way that landmarks can shift in the map is often non-linear, which is why the Extended Kalman Filter is used.
The main drawback of the Kalman Filter is the complexity. More landmarks can make SLAM more accurate, but Kalman filters can become too slow when the number of landmarks grows.

## Slide 17: Monocular SLAM
Recent research has demonstrated successful SLAM with a single monocular camera
  LSD-SLAM
  ORB-SLAM
Monocular cameras are still not as reliable as depth data from LiDar or stereo cameras, but SLAM is still possible with a single camera

## Slide 18: Dead Reckoning
Estimates a position based on the change from a previous position
Does not require maps or outside references
Utilizes sensor data and the precise physical measurement of the robot
Notes: Dead reckoning is a way for a robot to estimate its position using only sensors that are available on the robot
Other techniques for determining a robot’s location require maps or external references like GPS or signal strength
Dead reckoning is useful because it can be performed even when the robot is in unfamiliar territory and is unable to communicate.
In order to successfully estimate a position, the robot can use its sensors to estimate how far it has traveled.
The physical dimensions of the robot, the size of its wheels, and the layout of the wheels is important for dead reckoning algorithms.

## Slide 19: Humans and Dead Reckoning
Humans can estimate their position by counting their steps and multiplying by the size of each step
Most people, however, estimate their distance traveled based on how long they have been walking and how fast they typically walk
Notes: When a detailed map is not available, humans typically rely on dead reckoning to estimate how close they are to their goal.
However, humans often struggle with estimating their direction in the absence of external cues.
When people give directions, they often explain the path in terms of a dead reckoning system. For example:
  “Go five minutes down the road”
  “Turn right then take ten steps”

## Slide 20: Jetbot Path Planning
We can collect data using the camera images and train on areas of the image that the Jetson should follow, then build a regression model
This is useful for paths, racetracks and room navigation
See the Road Following secion in the Jetbot Notebooks. . Work through the Notebooks to:
  Collect and label the data, be sure to collect data off the path and pointing back to the path so that the Jetbot knows how to get back on track
  Train the model
  Optimize the model with TensorRT
  Load and run the model to see the Jetbot in action
The road following notebooks can be accessed directly on the Jetbot image or at the Github site https://github.com/NVIDIA-AI-IOT/jetbot/tree/master/notebooks/road_following

## Slide 21: Lab Community Project- Combine Collision Avoidance and Road Following
This community project combines the Collision Avoidance and Road Following Jupyter Notebooks and was contributed by community member Abu Abuelgasimsaadeldin
You can access this notebook at https://github.com/abuelgasimsaadeldin/Jetbot-Road-Following-and-Collision-Avoidance/blob/main/combine_scripts/RoadFollowing%2BCollisionAvoidance.ipynb

## Slide 22: Navigation Using ROS2 and Gazebo
ROS2 acts a middleware to work with robots such as the Jetbot to enable greater degree of control and automation
For those who do not have a Jetbot but have Jetson Nano, you can use ROS2 and Gazebo to work with a virtual jetbot.
For more information, refer to https://github.com/dusty-nv/jetbot_ros.

## Slide 23
Thank You
Edge AI and Robotics Teaching Kit